## Slide 1: Laboratory practices
By: Mašek Lukáš & bence balázs Tóth

## Slide 2: Parts of presentation
1/ Mircrobiological analysis of the diary products by: Bence Balázs Tóth
2/ Determination of total water hardness via chelatometry by: Mašek Lukáš

## Slide 3: 1/ Mircrobiological analysis of the diary products
Overall goal of the experiment - To determine the number of microorganism present in diary products.
Accomplished by: - Counting the amount of grown colonies on the media plate

## Slide 4: Required equipment
Diary product: - Milk
Chemicals: - GTKA agar medium, physiological solution
Tools - Petri dishes (2x), Test tubes (3x), Pipettes (1ml and 10ml and 100 µl ones), Microbiological hockey stick

## Slide 5: Process
(1) Take out 1ml of milk in a pipette
(2) Put the 1ml of milk in a test tube with 9ml of Physicological solution and shake the mixture together (dilution is now 10-1)
(3) Dilute the mixture two more times (to 10-2 and 10-3)
(4) Spread the GTKA agar solution in 2 petri dishes and leave it to stiffen
(5) Inoculum a pair of petri dishes with GTKA agar medium by the 100 µl 10-3 milk sample
(6) Spread it with the microbiological hockey stick
(7) Repeat step 5 and 6 one more time
(8) Put the two petri dishes in the incubator for 48 hour on 37 degrees celsius
(9) See the results after 48 hours.

## Slide 6: Results
The microorganisms had multiplied in number and grown all over the cultur plate.

## Slide 8: 2/ Determination of total water hardness via chelatometry
Overall goal of the experiment
- Determine in mmol.l-1 the total water hardness.
- Determine in mg.l-1 the calcium and magnesium content in drinking water

## Slide 9: Required equipment
Tools:
- burette, pipette, titration flasks, graduated cylinder
Chemicals:
-chelaton 3, dampening ammonia solution, Eriochromium black T, NaOH, murexid indicator

## Slide 10: Process
(1) Prepare 250 ml of chelaton with the concentration of 0,05 mol.l-1.
(2) Calculate the real concentration of chelaton.
(3) Pipette 100 ml of tested water into a titration flask.
(4) Add 5 of dampening ammonia solution by a graduated cylinder.
(5) Add a small amount of Eriochromium black T and titrate from wine red to blue colouring which lasts for 1 min.
(6) Determine 3x.
(7) Calculate water hardness in mmol.l-1.

## Slide 11: Calculation
m(g) = c * V * M m (real) = 4,6390 g V1 = 6,7 ml
m(g) = 0,05 * 0,25 * 372,24 V2 = 6,5 ml
m(g) = 4,653 g. V3 = 6,8 ml
Ø = 6,6 ml
c(real) = c(theoretical) * m(real) / m(theoretical)
c(real) = 0,05 * 4,6390/4,6530
c(real) = 0,04985 mol/l-1.

## Slide 12: Calculation
c = 0,04985 * 0,00666/0,1 * 1000 Ca: V1 = 5,3 ml
c = 3,3200 mmol.l-1 V2 = 5,5 ml
V3 = 5,6 ml
cca = 0,04985 * 0,005466 / 0,1 * 1000 Ø = 5,466 ml
cca = 2,7248 mmol.l-1
3,3200 – 2,7248 = 0,5952 mmol.l-1
0,5952 * 24,30 = 14,46336 mg
2,7248 * 40 = 108,992 mg

## Slide 13
THE END